## Slide 1: Acceptance Sampling
MEC-15
Outline
Need for Acceptance Sampling
Sampling Plan
Representative Sampling
Understanding the Concept
Probability and Acceptance Sampling
AQL & LTPD, -Risk & -Risk
OC Curve
How to work out an Acceptance Pla n
Readings
PMBoK, page 240-250.
Rita, page 309.
Reid Ch 6.
Krajewski, Supplement G.
Heizer, Ch 6.
Class Notes.

## Slide 2: Why Acceptance Sampling?
Acceptance Sampling refers to the process of randomly inspecting or testing a certain number of items from a Lot or Batch in order to decide whether to accept or reject the entire Lot or Batch
Is
d< c?
Accept the LOT
Yes
Reject the LOT
No
Acceptance Sampling done because:
  Inspection/Testing of entire Lot time-consuming, overly expensive and even, at times, impracticable
  Some testing, if not most, is destructive
n
Sample
Defectives (d) in Sample
LOT
N
Permissible Number (c) of Defectives
Notes: Agile, Waterfall

## Slide 3: Sampling Plan
Sampling is done to a plan, called the Acceptance Sampling Plan
A Sampling Plan precisely specifies the parameters of the sampling process and the acceptance/rejection criteria, in terms of:
  Size of the Lot (N)
  Size of the Sample picked randomly from the lot (n)
  The number of defectives in the Sample above which the Lot will be rejected (c)
  The number of sample that will be drawn
Types:
  Single
  Double
  Multiple/Sequential
Acceptance is at the confluence of Quality Management, Risk Management and Monitoring & Control
Notes: Agile, Waterfall

## Slide 4: “Representative” Sample
Sampling assumes a “Representative” Sample i.e. the proportion of defectives in the Lot is reflected in the Sample. If the Lot has d% defectives, the Sample is also expected to have d% defectives
“Unrepresentative” Sample has following implications:
  If Sample has less than d% defectives, MORE the chances of its acceptance (disadvantage to the Customer)
  If Sample has more than d% defectives, LESS the chances of its acceptance (disadvantage to the Supplier)
Notes: Agile, Waterfall

## Slide 5: Understanding the Concept … 1/2
A consignment of 10,000 bricks is ready at the brick kiln for transportation to the project site. As per the scope, the bricks must clear the 1,500 psi breaking strength. It is expected that there will be no more than 5% (500) weak bricks in the LOT. The SAMPLE acceptance plan calls for subjecting a random 100 brick single SAMPLE to the breaking strength. The entire LOT will be accepted if the number of brick failing the test is 5 or less. The entire LOT will be rejected if more than 5 bricks fail the test. In this case: Lot Size (N) = 10,000, sample size (n) = 100 and Acceptance Level (c) = 5
  Assume there are actually 90 defective bricks in the entire lot. Customer obviously does not know about them. Most likely, the supplier would not know it either. But it is a GOOD LOT
  If all the 90 defective bricks fall into the SAMPLE of 100, the entire GOOD LOT will be rejected. Rejecting a GOOD LOT is committing a Type 1 Error! Type-1 Error is unfair to the supplier
  The risk of a Type 1 Error occurring is known as the -risk
Notes: Agile, Waterfall

## Slide 6: Understanding the Concept … 2/2
  Assume there are actually 600 defective bricks in the entire LOT. Customer obviously does not know about them. Most likely, the supplier would not know it either. But it is a BAD LOT
  If none of the 600 defective bricks fall into the SAMPLE of 100, the entire LOT will be accepted. Accepting a BAD LOT is committing a Type 2 Error! A Type 2 Error is unfair to the buyer
  The risk of a Type 2 Error occurring is known as the -risk
  Acceptance Sampling is all about managing N, n, c, -risk, -risk, and two associated quantities AQL and LTPD which reflect the production Quality Standards
Notes: Agile, Waterfall

## Slide 7: Probability and Acceptance Sampling … 1/3
Consider a lot with 10,000 balls, mostly GREEN but some RED. A random SAMPLE of 100 balls is taken. What is the probability that less than 3 balls are RED?
where n=sample size, p=overall prob of an outcome, x=desired result
c. Here, n=100, c=2 (x=2,1,0)
Considerations:
More the RED balls in the LOT, greater their probability of making it to the SAMPLE. So, proportion of RED balls in the LOT is important
Probability success conditions are: 2 RED balls or 1 RED ball or No RED ball in the SAMPLE of 100; ie P(2R)+P(1R)+P(0R)…a case of Cumulative Probability, found by Binomial or Poisson Distribution:
Notes: Agile, Waterfall

## Slide 8: Probability and Acceptance Sampling … 2/3
Number of RED balls in the LOT (p) | Proportion of RED balls in the LOT (p) | Probability of less than 3 RED balls in the SAMPLE
0 | 0% | 1.000
100 | 1% | 0.920
200 | 2% | 0.677
300 | 3% | 0.423
400 | 4% | 0.238
500 | 5% | 0.125
600 | 6% | 0.062
700 | 7% | 0.030
800 | 8% | 0.014
900 | 9% | 0.006
1,000 | 10% | 0.003
As the proportion of RED Balls in the LOT increases, the SUCCESS PROBABILITY (< 3 RED balls in the SAMPLE) decreases
What if the GREEN balls represented GOOD items in a LOT and the RED balls represented the DEFECTIVES? The analogy provides the basis of the concept of ACCEPTANCE SAMPLING in which the Probability Curve becomes the Operating Characteristic (OC) Curve
Notes: Agile, Waterfall

## Slide 9: Probability and Acceptance Sampling … 3/3
Good LOT Bad LOT
Chart: Proportion (Fraction) of Defective Items
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
Probability of Acceptance (P) | 1 | 0.9197 | 0.67668 | 0.42319 | 0.2381 | 0.12465 | 0.061969 | 0.029636 | 0.013754 | 0.0062322 | 0.0027694
①  = 0.05=5% ↕
① 5% -Risk implies that there is 5% chance of REJECTING a GOOD LOT, or, 95% chance of ACCEPTING it, by the Buyer, at n=100 & c=2
② For 5% -Risk, at n=100 & c=2, the Seller/Producer has to meet the Quality standard of no more than 0.75 % defectives. This standard is called AQL
② 0.75%
③ Conversely, if the Seller/Producer can only meet the Quality Std of, say, 2%, then at n=100 & c=2, there will be just 68% probability of its acceptance, or the -Risk will be 32% ④
③
④=0.68=68%
⑤ 10% -Risk implies that there is 10% chance of ACCEPTING a BAD LOT, by the Buyer, at n=100 & c=2
⑥ Buyer’s 10% -Risk, at n=100 & c=2, will be satisfied so long as the Quality standard of no less than 5.2% is met. This standard is called LTPD.
⑦ Conversely, if the Buyer will not accept any Quality Std less than, say, 4.5%, then at n=100 & c=2, there will be 17.0% probability of accepting a BAD LOT, or - Risk will be 17.0% ⑧
⑥
5.3%
⑦ 4.5%
⑧ =0.17=17.0%
⑤  = 0.10= 10 %
↕
A Sampling Plan meets the requirements of -Risk, - Risk, AQL & LTPD through careful manipulation of ‘n’ and ‘c’
Notes: Agile, Waterfall

## Slide 10: Conclusions on the Discussion So Far
-Risk (Type-1 Error) has to do with the AQL and the Seller, or vice versa i.e. A certain -Risk implies a certain minimum quality standard (AQL) of production, or maximum number of defectives, which the Seller has to maintain. Conversely, a Seller maintaining a certain quality level (AQL) will be taking a corresponding risk (-Risk)
-Risk (Type-2 Error) has to do with the LTPD and the Buyer, or vice versa i.e. A certain -Risk implies Buyer’s TOLERANCE for a particular quality level (LTPD) which is lower than AQL. Conversely, a Buyer’s TOLERANCE for a particular quality level (LTPD) translates into a certain -Risk for him
Top portion of the OC Curve relates to -Risk, the AQL and the Seller
Bottom Portion of the OC Curve relates to -Risk, the LTPD and the Buyer
Defectives translate into following Quality Standards
Defects per 1000 (‰) | Defects Percent (%) | Quality Standard
617 | 62 | 0.5 Sigma
317 | 32 | 1.0 Sigma
134 | 13 | 1.5 Sigma
45 | 4.5 | 2.0 Sigma
12 | 1.2 | 2.5 Sigma
2.7 | 0.27 | 3.0 Sigma
Notes: Agile, Waterfall

## Slide 11: AQL & LTPD
Acceptance Quality Level (AQL)
  The small percentage of defectives a Consumer is willing to ACCEPT in a lot. Generally, 1-2%. For example, in this case, the Customer may be willing to accept 1%, i.e. 100 defectives. This is AQL
  Simply put, AQL is the quality level BELOW which a Consumer will ACCEPT the LOT
Lot Tolerance Percent Defective (LTPD), or Rejection Quality Level (RQL)
  A percentage of defectives BEYOND which the customer will REJECT the LOT
  LTPD/RQL is higher than the AQL but the Quality represented by LTPD/RQL is lower than the quality represented by AQL
Between the AQL and the LTPD/RQL, a customer may chose to:
  Accept the Lot for certain reasons, like trading quality for time. For example, the Customer may be willing to accept 5% defective bricks, i.e. 500 on the structural engineer’s advice that 500 “weaker” bricks in 10,000 will have negligible effect on the structure; 500 then is the LTPD/RQL
  Reject the Lot for safety reasons or for critical items, like parachutes, diving sets
  Do Multiple/Sequential Sampling and, based on the results thereof, Accept or Reject the LOT
  (all this is depicted in the next slide)
Notes: Agile, Waterfall

## Slide 12: AQL & LTPD
Percent Defectives in the Lot
AQL
ACCEPT
LTPD
REJECT
ACCEPT
or
REJECT
Reject!
This will be Type-1 Error
Chance of this happening is -Risk
Accept!
This will be Type-2 Error
Chance of this happening is -Risk
Accept or Reject, depending on:
certain reasons/ circumstances
Results of Multiple/ Sequential Sampling
Notes: Agile, Waterfall

## Slide 13: -Risk, -Risk
Adequate safeguards need to be incorporated in Acceptance Sampling to safeguard the interests of the Customer and the Supper, against the risk of the “Unrepresentative” Sample. This is done through -Risk and -Risk, both expressed as a probability or percentage
-Risk (Supplier’s Risk/Type-I Error) is the risk that the Customer will REJECT a LOT with the number of defectives EQUAL or LESS than the AQL. -Risk is usually taken as 5%
-Risk (Customer’s Risk/Type-2 Error) is the risk that the Customer will ACCEPT a LOT with the number of defectives MORE than the LTPD.  -Risk is usually taken as 10%
Notes: Agile, Waterfall

## Slide 14: OC Curve … 1/2
The Operating Characteristic (OC) Curve links all the parameters of the Acceptance Sampling Plan: N, n, c, AQL and LTPD, to determine the -Risk and -Risk
The curve helps manipulate the sample size (n) and the acceptance figure (c) to help bring the -Risk and -Risk within acceptable limits
More the defective items, greater the chance of their appearing in the Acceptance Sample and, therefore, less the chance of their acceptance by the Customer
The curve is constructed using possible Percent Defectives (along the X-axis) and the Probabilities (along the Y-axis)
We’ll use the probabilities from the Poisson Tables, which is structured like this:
c
np=λ
(Poisson Mean)
Probabilities
Notes: Agile, Waterfall

## Slide 15: OC Curve … 2/2
Poisson gives the chance (probability) of there being ‘c’ or less defectives in the sample ‘n’ if there are ‘p’ percent defectives in the Lot
for example: if overall there are 2% defectives in an entire Lot, and a sample of 120 is taken, then there is a 0.779 (78%) chance that there will be 3 or less defectives in a sample
Since ‘c’ or less defectives in the sample means the Sample, and hence the Lot is acceptable, the probability directly means acceptance. In this case, there is a 78% chance that there are 3 or less defectives in the Sample; since the Sample, and hence the Lot must be accepted if there are 3 or less defectives, it implies that there is a 78% chance of accepting the Lot
If there is 78% chance of acceptance, there is 100-78=22% chance of rejecting the Sample and the Lot
Poisson gives acceptance probability figures for the product ‘np’ under various values of ‘c’. The product ‘np’ is also called the Poisson Mean ()
Notes: Agile, Waterfall

## Slide 16: Complete Acceptance Sampling Plan & OC Curve … 1/5
An order for supply of 2,000 electrical fans has been placed on a Supplier. The agreed acceptance sampling plan calls for a random sample of 120 fans with an acceptance level of 3. AQL has been settled at 2% defectives. The worst quality that the Project Manager can tolerate is 6% defectives in the lot.
What is the risk/chance that a GOOD LOT of fans supplied by the Supplier will be REJECTED by the Project Manager, and a BAD LOT supplied by the Supplier will be ACCEPTED by the Project Manager?
N=2,000 n=120 c=3 | AQL = 2% = 0.02 -Risk = ? | LTPD =6% = 0.06 -Risk = ?
Notes: Agile, Waterfall

## Slide 17: Complete Acceptance Sampling Plan & OC Curve … 2/5
Proportion Defective (p) | np=λ | Probability (P) of c or less defectives (Probability of ACCEPTING the LOT) | Probability of REJECTING the LOT | Risks
0.01 | 1.2 | 0.966 |  | 
0.02 (AQL) | 2.4 | 0.779 | 1-0.779 = 0.221 |  = 0.221 = 22.1%
0.03 | 3.6 | 0.515 |  | 
0.04 | 4.8 | 0.294 |  | 
0.05 | 6.0 | 0.151 |  | 
0.06 (LTPD) | 7.2 | 0.072 |  | =7.2%
0.07 | 8.4 | 0.032 |  | 
0.08 | 9.6 | 0.014 |  | 
0.09 | 10.8 | 0.006 |  | 
0.10 | 12.0 | 0.002 |  | 
N=2,000 n=120, c=3 | AQL = 2% = 0.02 -Risk = ? | LTPD = 6% = 0.06 -Risk = ?
Bad Lot
Good Lot
p is the x-axis of the OC curve
P is the y-axis of the OC curve
Notes: Agile, Waterfall

## Slide 18: Complete Acceptance Sampling Plan & OC Curve … 3/5
Chart: Proportion (Fraction) of Defective Items
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
Probability of Acceptance | 1 | 0.966 | 0.779 | 0.515 | 0.294 | 0.151 | 0.072 | 0.032 | 0.014 | 0.006 | 0.002
 = 1-0.779
= 0.221
 = 0.072
Notes: Agile, Waterfall

## Slide 19: Complete Acceptance Sampling Plan & OC Curve … 1/5
In the previous example, if the Supplier is not willing to take more than 5% risk that his supplied GOOD LOT will be REJECTED by the Project Manager, and the Project Manager is not willing to take more than 10% risk that he will ACCEPT a BAD LOT landed by the Supplier, then the given plan does not meet the Supplier’s risk limits. At 22.1%, -Risk is well outside the Supplier limit of 5%
At 7.2 %,  -Risk is well inside the Consumer limit of 10%
n & c have to be adjusted to meet the limits of both the risks; say n is increased to 200 (from 120) and c to 7 (from 3)
N=2,000 n=120→200 c=3→7 | -Risk = 5% = 0.05 AQL = 2% = 0.02 | -Risk = 10% = 0.10 LTPD =6% = 0.06
Notes: Agile, Waterfall

## Slide 20: Complete Acceptance Sampling Plan & OC Curve … 4/5
Proportion Defective (p) | n = 120, c = 3 |  | 
 | λ=np | Probability of c or less defectives | Remarks
0.01 0.02 (AQL) 0.03 0.04 0.05 0.06 (LTPD) 0.07 0.08 0.09 0.10 | 1.2 2.4 3.6 4.8 6.0 7.2 8.4 9.6 10.8 12.0 | 0.966 0.779 0.515 0.294 0.151 0.072 0.032 0.014 0.006 0.002 |  = 0.221 
N=2,000 n=120  200 c=3  7 | -Risk = 5% = 0.05 AQL = 2% = 0.02 | -Risk = 10% = 0.10 LTPD = 6% = 0.06
n = 200, c = 7 |  | 
λ=np | Probability of c or less defectives | Remarks
2.0 4.0 6.0 8.0 10.0 12.0 14.0 16.0 18.0 20.0 | 0.999 0.949 0.744 0.453 0.220 0.090 0.032 0.010 0.003 0.001 |  = 0.051 
Notes: Agile, Waterfall

## Slide 21: Complete Acceptance Sampling Plan & OC Curve … 5/5
Chart: Proportion (Fraction) of Defective Items
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
 | 1 | 0.966 | 0.779 | 0.515 | 0.294 | 0.151 | 0.072 | 0.032 | 0.014 | 0.006 | 0.002
 | 1 | 0.999 | 0.949 | 0.744 | 0.453 | 0.22 | 0.09 | 0.032 | 0.01 | 0.003 | 0.001
The Supplier’s Risk (-Risk) has reduced to 5.1% from the previous 22.1%
The Consumer’s Risk ( -Risk) has increased to 9.0% from the previous 7.2%, but still within limits
By adjusting the Sample Size (n) and the Acceptance Level (c), the Supplier’s and Consumer’s risk have modified as follows:
n=120, c=3
n=200, c=7
By fine-tuning the curve, the risks cannot be brought down into exact limits. In this case, n=196 and c=7 will return an -Risk of 4.6% and -Risk of 9.9%, both of which are within limits and offer a perfect combination
Notes: Agile, Waterfall

## Slide 22: Effect of Changing ‘n’ & ‘c’ on Acceptance Sampling … 1/3
A project manager has received a shipment of 1,000 items for the project. The sampling plan for inspecting these items calls for a sample size n=60 and an acceptance number c=1. The contract with the supplier calls for an AQL of 1 defective item per 100 and an LTPD of 6 defective items per 100. Construct the OC curve for this plan, and determine the supplier’s and the consumer’s risk for the plan
N=1,000 n=60 c=1 | AQL = 1% = 0.01 | LTPD = 6% = 0.06
Notes: Agile, Waterfall

## Slide 23: Effect of Changing ‘n’ & ‘c’ on Acceptance Sampling … 2/3
Proportion Defective (p) | np=λ | Probability of c or less defectives | Remarks
0.01 (AQL) 0.02 0.03 0.04 0.05 0.06 (LTPD) 0.07 0.08 0.09 0.10 | 0.6 1.2 1.8 2.4 3.0 3.6 4.2 4.8 5.4 6.0 | 0.878 0.663 0.463 0.308 0.199 0.126 0.078 0.048 0.029 0.017 | 1-;  = 1-0.878 = 0.122 
N=1,000 n=60 c=1 | AQL = 1% = 0.01 | LTPD = 6% = 0.06
Notes: Agile, Waterfall

## Slide 24: Effect of Changing ‘n’& ‘c’ on Acceptance Sampling … 1/3
Chart: Proportion (Hundredth Fraction) of Defective Items
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
Probability of Acceptance | 1 | 0.878 | 0.663 | 0.463 | 0.308 | 0.199 | 0.126 | 0.078 | 0.048 | 0.029 | 0.017
 | c | n |  |  | 
 | 1 | 60 | 0.122 | 0.126 | 
Notes: Agile, Waterfall

## Slide 25: Effect of Changing ‘n’ on Acceptance Sampling … 1/2
p | n = 60 |  | n = 80 |  | n = 100 |  | n = 120 | 
 | np=λ | Prob | np=λ | Prob | np=λ | Prob | np=λ | Prob
0.01 (AQL) 0.02 0.03 0.04 0.05 0.06 (LTPD) 0.07 0.08 0.09 0.10 | 0.6 1.2 1.8 2.4 3.0 3.6 4.2 4.8 5.4 6.0 | 0.878 0.663 0.463 0.308 0.199 0.126 0.078 0.048 0.029 0.017 | 0.8 1.6 2.4 3.2 4.0 4.8 5.6 6.4 7.2 8.0 | 0.809 0.525 0.308 0.171 0.092 0.048 0.024 0.012 0.006 0.003 | 1.0 2.0 3.0 4.0 5.0 6.0 7.0 8.0 9.0 10.0 | 0.736 0.406 0.199 0.092 0.040 0.017 0.007 0.003 0.001 0.000 | 1.2 2.4 3.6 4.8 6.0 7.2 8.4 9.6 10.8 12.0 | 0.663 0.308 0.126 0.048 0.017 0.006 0.002 0.001 0.000 0.000
N=1,000 n=60, 80, 100, 120 c=1 | AQL = 1% = 0.01 | LTPD = 6% = 0.06
Increasing the Sample Size increases the Supplier’s Risk and reduces the Customer’s Risk
Notes: Agile, Waterfall

## Slide 26: Effect of Changing ‘n’ on Acceptance Sampling … 2/2
Chart: Proportion (Fraction) of Defective Items
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
Probability of Acceptance | 1 | 0.878 | 0.663 | 0.463 | 0.308 | 0.199 | 0.126 | 0.078 | 0.048 | 0.029 | 0.017
 | 1 | 0.809 | 0.525 | 0.308 | 0.171 | 0.092 | 0.048 | 0.024 | 0.012 | 0.006 | 0.003
 | 1 | 0.736 | 0.406 | 0.199 | 0.092 | 0.04 | 0.017 | 0.007 | 0.003 | 0.001 | 0
 | 1 | 0.663 | 0.308 | 0.126 | 0.048 | 0.017 | 0.006 | 0.002 | 0.001 | 0 | 0
n=60, c=1
n=80, c=1
n=100, c=1
n=120, c=1
 | c | n |  |  | 
 | 1 | 60 | 0.122 | 0.126 | 
 | 1 | 80 | 0.191 | 0.048 | 
 | 1 | 100 | 0.264 | 0.017 | 
 | 1 | 120 | 0.332 | 0.006 | 
Increasing the Sample Size increases the Supplier’s Risk and reduces the Customer’s Risk
Notes: Agile, Waterfall

## Slide 27: Effect of Changing ‘c’ on Acceptance Sampling … 1/2
p | c = 1 |  | c = 2 | c = 3 | c = 4
 | np=λ | Prob | Prob | Prob | Prob
0.01 (AQL) 0.02 0.03 0.04 0.05 0.06 (LTPD) 0.07 0.08 0.09 0.10 | 0.6 1.2 1.8 2.4 3.0 3.6 4.2 4.8 5.4 6.0 | 0.878 0.663 0.463 0.308 0.199 0.126 0.078 0.048 0.029 0.017 | 0.977 0.879 0.731 0.570 0.423 0.303 0.210 0.143 0.095 0.062 | 0.997 0.966 0.891 0.779 0.647 0.515 0.395 0.294 0.213 0.151 | 1.000 0.992 0.964 0.904 0.815 0.706 0.590 0.476 0.373 0.285
N=1,000 n=60 c=1, 2, 3, 4 | AQL = 1% = 0.01 | LTPD = 6% = 0.06
Increasing the Acceptance Level reduces the Supplier’s Risk and increases the Customer’s Risk
Notes: Agile, Waterfall

## Slide 28: Effect of Changing ‘c’ on Acceptance Sampling … 2/2
Chart: Proportion (Fraction) of Defective Items
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
Probability of Acceptance | 1 | 0.878 | 0.663 | 0.463 | 0.308 | 0.199 | 0.126 | 0.078 | 0.048 | 0.029 | 0.017
 | 1 | 0.977 | 0.879 | 0.731 | 0.57 | 0.423 | 0.303 | 0.21 | 0.143 | 0.095 | 0.062
 | 1 | 0.997 | 0.966 | 0.891 | 0.779 | 0.647 | 0.515 | 0.395 | 0.294 | 0.213 | 0.151
 | 1 | 1 | 0.992 | 0.964 | 0.904 | 0.815 | 0.706 | 0.59 | 0.476 | 0.373 | 0.285
n=60, c=1
n=60, c=2
n=60, c=3
n=60, c=4
c | n |  | 
1 | 60 | 0.122 | 0.126
2 | 60 | 0.023 | 0.303
3 | 60 | 0.003 | 0.515
4 | 60 | 0.000 | 0.706
Increasing the Acceptance Level reduces the Supplier’s Risk and increases the Customer’s Risk
Notes: Agile, Waterfall

## Slide 29: Finding ‘n’ & ‘c’ by Trial & Error … 1/5
A project manager is negotiating sampling plan for procurement of 1,000 items for the project. An AQL of 30 defectives in the entire lot has already been settled. Project Manager’s LTPD is 80 or more defectives in the lot.
Assuming that the vendor will not accept a 5% risk that the Project Management will REJECT his good lot (defectives in the lot AQL or less), and the Project Manager will not take more than 10% risk that he will ACCEPT a bad lot (defectives in the lot more than the LTPD), give at least two combination figures for Sample Size and Sample Acceptance Level.
N=1,000 n=?, c=? | AQL = 30/1,000 = 3% = 0.03 -Risk = 5% | LTPD = 8/1,000 = 8% = 0.08 -Risk = 10%
Notes: Agile, Waterfall

## Slide 30: Finding ‘n’ & ‘c’ by Trial & Error … 2/5
Chart: 
Series 1 | 0.966 | 0.957 | 0.951 | 0.963 | 0.975 | 0.967
Series 2 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95
Series 3 | 0.313 | 0.077 | 0.092 | 0.065 | 0.179 | 0.056
Series 4 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
-Risk
-Risk
0.950
0.010
n=100
n=200
n=180
n=220
n=160
n=240
c=6 ✗
c=10 ✓
c=9 ✓
c=11 ✓
c=9✗
c=12 ✓
np @ AQL=0.03 |  |  |  |  |  | 
nP @ LTPD=0.08 |  |  |  |  |  | 
n |  |  |  |  |  | 
3.0
8.0
100
6.0
16.0
200
5.4
14.4
180
6.6
17.6
220
4.8
12.8
160
7.2
19.2
240
Notes: Agile, Waterfall

## Slide 31: Finding ‘n’ & ‘c’ by Trial & Error … 3/5
TARGETS→ | P of λAQL |  |  |  |  |  | > 0.95 |  | P of λLTPD < |  |  |  |  | < 0.10 |  | 
p |  | P |  |  |  |  |  |  |  |  |  |  |  |  |  | 
P @ AQL=0.03 |  | .966 | .957 | .951 | .963 | .975 |  | .967 |  |  |  |  |  |  |  | 
P @ LTPD=0.08 |  | .313✗ | .077✓ | .092✓ | .065✓ | .179✗ |  | .056✓ |  |  |  |  |  |  |  | 
n→ |  | 100 | 200 | 180 | 220 | 160 |  | 240 |  |  |  |  |  |  |  | 
c→ |  | 6 | 10 | 9 | 11 | 9 |  | 12 |  |  |  |  |  |  |  | 
 |  | ✗ | ✓ | ✓ | ✓ | ✗ |  | ✓ |  |  |  |  |  |  |  | 
Make an assumption for n. 100 is a good starter
Find λ=np at AQL and LTPD. Call them λAQL and λLTPD
Enter the Poisson Tables with λAQL and find a probability which is (1-AQL) or more. Note the value of c
Go down the same column and note the probability for λLTPD.
If the probability of λLTPD is more than LTPD, increase or decrease n until the right probabilities have been found: bearing in mind that increase in n decreases -Risk and vice versa
It should be possible to come to the right combination of n and c in 3-4 trials
Following table may be helpful
Notes: Agile, Waterfall

## Slide 32: Finding ‘n’ & ‘c’ by Trial & Error … 4/5
A project manager is planning sampling for a certain bulk procurement item. The Supplier, who is also the manufacturer, produces items at a quality level which is equivalent to no more than 1% defectives. The Project Manager will tolerate up to 4% defectives in the lot.
If the Supplier’s and the Project Manager’s risk is to be no more than 5% each, suggest at least two combinations of sample size and acceptance level which will satisfy both the Supplier’s and Project Manager’s risk limits.
n=? c=? | AQL = 1% = 0.01 -Risk = 5% | LTPD = 4% = 0.04 -Risk = 5%
Notes: Agile, Waterfall

## Slide 33: Finding ‘n’ & ‘c’ by Trial & Error … 5/5
Chart: 
Series 1 | 0.981 | 0.983 | 0.979 | 0.966 | 0.976 | 0.977
Series 2 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95
Series 3 | 0.433 | 0.191 | 0.022 | 0.046 | 0.071 | 0.039
Series 4 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
-Risk
-Risk
n=100
n=200
n=400
n=300
n=280
n=340
c=3 ✗
c=5 ✗
c=8 ✓
c=6 ✓
c=6 ✗
c=7 ✓
np @ AQL=0.01 |  |  |  |  |  | 
np @ LTPD=0.04 |  |  |  |  |  | 
n |  |  |  |  |  | 
1.0
4.0
100
2.0
8.0
200
4.0
16.0
400
3.0
12.0
300
2.8
11.2
280
3.4
13.6
340
0.950
0.050
Notes: Agile, Waterfall